EPBP OPCODE LIST
key:
priority is 1 through 5, 5 means low priority, 1 means high.
Reg is normal register. [reg] is register indirect address. Imm is immediate. It is assumed this is a dword, if not dword, then immb or immw or immd for byte word and dword respectively. [iptr] means immediate pointer to address. Immdc is 32bit absolute code address immediate. Immdcr is a 32bit relative code address immediate. There is also immwcr, and immbwcr. There isAll opcodes are expanded. Immbc is relative byte code address, As is immwc. Immf is a 32bit float immediate.
Reg represents both the float set of registers and integer set. If the top bit is 0 in the reg byte, it uses the integer set, if 1, then it uses float set.
For functions that are integer or float only, they should be prefixed with I or f.
whenever using [reg] the top bit determines if the memory points to an int or a float. Floats are always 32bit. So

Addressing modes:
there are a few different methods. [reg] is indirect register. [reg+reg] is register indirect with register displacement. [iptr+reg] is immediate pointer with register displacement. [reg+[reg]] is register indirect with a register indirect displacement. [reg+imm8] is register indirect with 1 byte displacement.
Note: all addressing is assumed to be dword unless postfixed with b,w,d. Such as [reg]w or [iptr]b. If it is made this way, the other arguments must also have a postfix
also note: if it involves sign extending, an s is postfixed after the size postfix, such as mov regd immbs will sign extend immb

Opcode Name	Arg 1/target	Arg 2	Arg 3	Priority	Assigned Opcode #
Mov	Reg	Reg		1	0x11
Mov	[reg]	Reg		1
Mov	Regd	Immb		1
Mov	Regd	Immbs		3
Mov	Reg	[iptr]		1
Mov	[reg]	[iptr]		2
Mov	Regd	immd		1	0x10
Mov	[reg+reg]	Reg		2
Mov	[reg]	immd/f		1	0x14

Xchg	Reg	Reg		1
Xchg	[reg]	Reg		2
Xchg	[iptr]	Reg		3
Xchg	[reg]	[reg]		3

Push	Reg			1	0x12
Push	[iptr]d			1
Push	Immd			1
Push	[reg]d			1

Pop	Reg			1	0x13
Pop	[reg]d			1
Pop	[iptr]d			1

Add	Reg	Reg		2
Add	Reg	Reg	Reg	1
Add	Reg	Immb		2
Add	Reg	Reg	immb	1
Add	[iptr]b	immb		1
Add	[iptr]d	immbs		1
Add	Reg	Immd		2
Add	[reg+(reg1)]	[iptr+(reg1)	immb	2

Sub	Reg	Reg		2
sub	Reg	Reg	Reg	1
sub	Reg	Immb		2
sub	Reg	Reg	immb	1
sub	[iptr]b	immb		1
sub	[iptr]d	immbs		1
sub	Reg	Immd		2
sub	[reg+(reg1)]	[iptr+(reg1)]	immb	2

Mul	Reg	Reg		2
Mul	Reg	Immw		1
Mul	Reg	Reg	reg	1
Mul	[reg]	Reg	Reg	1
Mul	[iptr]	Reg	Reg	2
Mul	[reg]b	Immbs		1
Mul	[reg]d	[reg]bs		3
Mul	[reg+reg]	Immb		2

Div	Reg	Reg		2
Div	Reg	Immws		1
Div	[iptr]d	Reg		1
Div	Reg	Reg	Reg	1
Div	[reg]	Reg	Reg	1
Div	[iptr]	Reg	Reg	2
Div	[iptr]b	[reg]bs		3
Div	Reg	Reg	Immbs	1

Mod	Reg	Reg		2
Mod	Reg	Reg	Reg	1
Mod	Reg	[iptr]		2
Mod	Reg	Immw		1
Mod	Reg	Reg	Immb	1
Mod	[iptr]	Reg		2
Mod	[iptr]d	Immb		2

Cdm	Reg	Reg	Reg	2
Cdm	Reg	Reg	Immb	2

Xcall	Reg	Immw		1
Xcall	0 (implicit)	Immw		1
Xcall	1(implicit)	Immw		1
Xcall	reg	Reg		1
Xcall	[reg]	Reg		2
Xcall	[reg]	[reg]		3
Xcall	[iptr]	Reg		1

Setbank	Immd			1
Setbank	[iptr]			2
Setbank	Reg			1
Setbank	[reg]			1

Getbank	Reg			1
Getbank	[reg]			2
Getbank	[iptr]			2

Jmp	immdc(abs)			1	0x50
Jmp	Immdcr			4
Jit	Immdc			1	0x60
Jif	Immdc			1	0x61
Jmp	Immbcr			2
Jmp	Immwcr			1
Jit	Immwcr			1
Jif	Immwcr			1
Jmp	xreg			4

Cls	Reg	Reg		1	0x80
Cls	Reg	Immd		2
Cls	[reg]	Reg		1
Cls	Reg	[iptr]		2
Cls	[iptr]b	Immb		2
Cls	[reg]	[reg]		2

Cle	Reg	Reg		1	0x81
Cle	Reg	Immd		2
Cle	[reg]	Reg		1
Cle	Reg	[iptr]		2
Cle	[iptr]b	Immb		2
Cle	[reg]	[reg]		2

Cgt	Reg	Reg		1	0x82
Cgt	Reg	Immd		2
Cgt	[reg]	Reg		1
Cgt	Reg	[iptr]		2
Cgt	[iptr]b	Immb		2
Cgt	[reg]	[reg]		2

Cge	Reg	Reg		1	0x83
Cge	Reg	Immd		2
Cge	[reg]	Reg		1
Cge	Reg	[iptr]		2
Cge	[iptr]b	Immb		2
Cge	[reg]	[reg]		2

Cne	Reg	Reg		1	0x84
Cne	Reg	Immd		2
Cne	[reg]	Reg		1
Cne	Reg	[iptr]		2
Cne	[iptr]b	Immb		2
Cne	[reg]	[reg]		2

Ceq	Reg	Reg		1	0x85
Ceq	Reg	Immd		2
Ceq	[reg]	Reg		1
Ceq	Reg	[iptr]		2
Ceq	[iptr]b	Immb		2
Ceq	[reg]	[reg]		2

Mov	TR(implicit)	Reg		1
Sttr (set TR)
Rttr (reset TR)
Mov	Reg	TR(implicit)

Or	Reg	Reg		2
Or	Reg	Reg	Reg	1
Or	Reg	Immd		2
Or	Regb	Immb		2
Or	[reg]	Reg		1
Or	[iptr]	Immd		3
Or	[reg]b	Immb		2
Or	Reg	[iptr]		1

xor	Reg	Reg		2
Xor	Reg	Reg	Reg	1
Xor	Reg	Immd		2
xor	Regb	Immb		2
xor	[reg]	Reg		1
xor	[iptr]	Immd		3
xor	[reg]b	Immb		2
xor	Reg	[iptr]		1

and	Reg	Reg		2
and	Reg	Reg	Reg	1
and	Reg	Immd		2
and	Regb	Immb		2
and	[reg]	Reg		1
and	[iptr]	Immd		3
and	[reg]b	Immb		2
and	Reg	[iptr]		1

--Not--	-target/source-	--source--	--	--	--
Not	Reg			1
Not	Reg	Reg		2
Not	[iptr]			1
Not	Reg	Immd		2
Not	Reg	[iptr]		2
Not	[reg]			1

Inc	Reg			1
Inc	[reg]			1
Inc	[iptr]d			2

Dec	Reg			1
Dec	[reg]			1
Dec	[iptr]d			2

Bswap	Reg			3
Bswap	[reg]			3
Bswap	[iptr]d			3
Bswap	Reg	Reg		3
Bswap	[reg]	Reg		3

Call	Immc			1
Call	Immwc			1

Ret				1

Movit	Reg	Reg		1
Movit	[reg]	Reg		1
Movit	Reg	[reg]		1
Movit	Reg	Immd		2
Movit	[iptr]b	Immb		1

Movif	Reg	Reg		1
Movif	[reg]	Reg		1
Movif	Reg	[reg]		1
Movif	Reg	Immd		2
Movif	[iptr]b	Immb		1

-Machid- / machine id	-return store-	-function-		--	--
Machid	Reg	Reg		1	1

Hlt				1	0xF4

Nop					0x00
Reserved					0xFF
Exit				1	0xFE
Ivld				1	0xBA